## Slide 1: Road Network Lahore

## Slide 2: METHODOLOGY
Google Map Images
Segmentation
Segmentation Masks
Width Information
Convert to graph
Thinning
Graphs
Georeference
Georeferenced Graphs
Distance Transform
Single Line Segmentation Masks
Merge
Threshold
GeoJson file
Issues
Manually resolving

## Slide 3: ISSUES
Discontinuity at boundaries while merging.
  Resolved (manually)

## Slide 4: ISSUES
False lines for main roads
  Resolving (manually)

## Slide 5: CLASSIFICATION OF ROADS
United States of America
  Arterials
    Interstates
    Other Freeways and Expressways
    Other Principal Arterials
    Minor Arterials
  Non-Arterials
    Collectors
    Local Roads
United Kingdom
  Special Roads (Motorways)
  “A” Roads
  “B” Roads
  Classified unnumbered “C” Roads
  Unclassified “U”

## Slide 6: CLASSIFICATION OF ROADS
India
  National Highways
  State Highways
  District Roads
  Rural Roads
  Urban Roads
  Project Roads
Sri Lanka
  Expressways
  National Roads
  Provincial Roads
  Local Authority Roads
  Other Road

## Slide 7: CLASSIFICATION OF ROADS
Pakistan (as per NTRC)
  Motorways
  Expressways
  National Highways
  Primary Roads
  Secondary Roads
  Local Roads

## Slide 8: ATTRIBUTES
Name
Length
Class
  Primary, Secondary, Local
Material
  Asphalt, Mud
Type
  Main, Overhead, Underpass, Service
U-Turn (binary)
Speed

## Slide 9: Future Directions
Imbed direction in network
  Methodology finalized
Help in labeling